## Slide 1: Unusually Formal Method: a Verilog program verifier
Sophia Zhang

## Slide 2: INTRODUCTION: HDLs
Hardware Description Language: language used to describe digital logic circuits
Gate level and higher-level abstractions
For simple and complex designs
module adder(a0, a1, b0, b1,
cout0, cout1);
input a0, a1, b0, b1;
output cout0, cout1;
assign cout0 = a0 ^ b0;
assign cout1 = (a1 ^ b1) ^ (a0 & b0);
endmodule
module adder(a, b, out);
input [1:0] a, b;
output [1:0] cout;
assign cout = a + b;
endmodule

## Slide 3: INTRODUCTION: Verification
Pre-silicon testing
Unit tests through UVM
Coverage tests
Profiling
Formal methods like model checking

## Slide 4: Motivation

## Slide 5: Motivation
Writing unit and coverage tests
  Lots of programming effort
  May not cover all test cases!
Formal verification
  Model checking and program abstraction
  Lots of programmer effort + knowledge needed
  Lots of resources + time

## Slide 6: Project Goals
A program verifier similar to Dafny
Supports formal verification through annotated post conditions within the Verilog language
Supports formal verification of bit-level combinational logic
  Outputs only involve the inputs no concept of state

## Slide 7: Implementation
Source code
Syntax Tree
Language Parser
Custom Z3 Boolean Converter
10+20*30
Z3 equivalent
mkAdd(10, mkMul(20,30))
…
#ensures(10+20*30==610)
Verilog.g4
Notes: Mention was unable to find a suitable Verilog parser so had to somewhat implement own

## Slide 8: Example: 2-Bit adder
module adder(a0, a1, b0, b1,
cout0, cout1);
input a0, a1, b0, b1;
output cout0, cout1;
assign cout0 = a0 ^ b0;
assign cout1 = (a1 ^ b1) ^ (a0 & b0);
//@ensures cout0 == a0 ^ b0 endmodule

## Slide 9: Example: 2-Bit adder
from z3 import *
a0 ,a1 ,b0 ,b1 = Bools('a0 a1 b0 b1')
cout0 ,cout1 = Bools('cout0 cout1')
cout0 = Xor((a0),(b0),)
cout1 = Xor((Xor((a1),(b1),)),(And((a0),(b0),)),)
from z3 import *
a0 ,a1 ,b0 ,b1 = Bools('a0 a1 b0 b1')
cout0 ,cout1 = Bools('cout0 cout1')
cout0 = Xor((a0),(b0),)
cout1 = Xor((Xor((a1),(b1),)),(And((a0),(b0),)),)
ensures = Not(cout0==Xor((a0),(b0)))
s = Solver()
s.add(cout0)
s.add(cout1)
s.add(ensures)
if s.check() == sat:
m = s.model()
print("found a counter example!")
else:
print("UNSAT so satisfied")

## Slide 10: Example: 2-Bit adder
module adder(a0, a1, b0, b1,
cout0, cout1);
input a0, a1, b0, b1;
output cout0, cout1;
assign cout0 = a0 ^ b0;
assign cout1 = (a1 ^ b1) ^ (a0 & b0);
//@ensures cout0 == a0 ^ b0 endmodule
from z3 import *
a0 ,a1 ,b0 ,b1 = Bools('a0 a1 b0 b1')
cout0 ,cout1 = Bools('cout0 cout1')
cout0 = Xor((a0),(b0),)
cout1 = Xor((Xor((a1),(b1),)),(And((a0),(b0),)),)
ensures = Not(cout0==Xor((a0),(b0)))
s = Solver()
s.add(cout0)
s.add(cout1)
s.add(ensures)
if s.check() == sat:
m = s.model()
print("SAT, exists a counterexample!")
else:
print("UNSAT so satisfied")
$python adder_v1.v.py
UNSAT so satisfied

## Slide 11: Example: 2-Bit adder
module adder(a0, a1, b0, b1,
cout0, cout1);
input a0, a1, b0, b1;
output cout0, cout1;
assign cout0 = a0 & b0;
assign cout1 = (a1 ^ b1) ^ (a0 & b0);
//@ensures cout0 == a0 ^ a1 endmodule
from z3 import *
a0 ,a1 ,b0 ,b1 = Bools('a0 a1 b0 b1')
cout0 ,cout1 = Bools('cout0 cout1')
cout0 = And((a0),(b0),)
cout1 = Xor((Xor((a1),(b1),)),(And((a0),(b0),)),)
ensures = Not(cout0==Xor((a0),(b0)))
s = Solver()
s.add(cout0)
s.add(cout1)
s.add(ensures)
if s.check() == sat:
m = s.model()
print(“SAT, exists a counterexample!")
else:
print("UNSAT so satisfied")
$ python adder_v1.v.py
SAT, exists a counterexample!

## Slide 12: Next Steps
Must Accomplish
Automate the ensures clause in verification
Allow for multiple ensures
Future Directions
Expand beyond single bit abstraction
Expand to sequential logic
Expand the abstraction to beyond gate level

## Slide 13: SUMMARY
UFM: Unusually formal method a formal program verifier for a subset of the Verilog language